## Slide 1
Functional/Effective Connectivity for fMRI
Rik Henson
MRC CBU, Cambridge

## Slide 2: Structural, functional & effective connectivity
Structural/anatomical connectivity = presence of axonal connections / white matter tracks (eg, DWI)
Functional connectivity = statistical dependencies between regional time series (eg, ICA)
Effective connectivity = causal (direct/directed) interactions between populations (eg, DCM) (based on explicit network models)

## Slide 3: Structural vs Functional connectivity
Tracing studies
Tractography from DWI
But functionally, effect of one neuron on another can depend on:
  Activity of a third (gating)
  Rapid changes in plasticity

## Slide 4
No connection between B and C,
yet B and C correlated because of common input from A, eg:
A = V1 fMRI time-series
B = 0.5 * A + e1
C = 0.3 * A + e2
Correlations:
A B C
1
0.49 1
0.30 0.12 1
A
B
C
0.49
0.31
-0.02
2=0.5, ns.
Functional connectivity
Effective connectivity
Functional vs Effective connectivity
Partial Correlation is approximate way

## Slide 5: Functional Connectivity (in fMRI)
State-based connectivity
  Time-Series Correlation (TSC), eg resting-state/movie, though could be spurious, e.g, cardio/respiratory; motion confounds..., or just reflection of structural connectivity...)
    Multivariate (whole-brain, voxel-wise) decomposition, eg PCA, ICA
    ROI(parcel)-based, pairwise connectivity
Task-Based connectivity
  Beta-Series Regression (BSR) or Psycho-Physiological Interactions (PPI)
Network-based models
  Dynamic Causal Modelling (DCM) (effective connectivity; not covered in notebooks)
  Graph-theory summaries of functional networks

## Slide 6
Matrix Factorisation (eg, SVD)
http://alexhwilliams.info/itsneuronalblog/2016/03/27/pca/
Voxels
Scans (Time/Subjects)
Spatial “networks”
Temporal “profile”

## Slide 7
http://alexhwilliams.info/itsneuronalblog/2016/03/27/pca/
1
2
3
Voxels
Scans (Time/Subjects)
Spatial “networks”
Matrix Factorisation (eg, SVD)
Temporal “profile”

## Slide 8: Multivariate fC
PCA is an SVD of a covariance matrix, assuming orthogonal components (e.g, spatial patterns across voxels)
ICA assumes components are independent (usually across space with fMRI, but could be across time) and has been shown more effective in (re)producing characteristic resting-state networks (RSNs), and separating signal from noise

## Slide 9: PCA vs ICA
Voxel 1
Voxel 2

## Slide 10: Multivariate fC
PCA is an SVD of a covariance matrix, assuming orthogonal components (e.g, spatial patterns across voxels)
ICA assumes components are independent (usually across space with fMRI, but could be across time) and has been shown more effective in (re)producing characteristic resting-state networks (RSNs), and separating signal from noise
There are other types of matrix factorisation (e.g., non-negative, tensor-based) that have been tried, as well as various clustering techniques
Incidentally, while PCA is an SVD of the data covariance matrix (Y’Y), other techniques like CCA and PLS are SVDs of data-model covariance (Y’X)…

## Slide 11: ICA RSNs
open.win.ox.ac.uk

## Slide 12: ICA RSNs
open.win.ox.ac.uk
ICA Noise components

## Slide 13: Multivariate fC
Group ICA, concatenate subjects or used Tensor ICA (e.g., , eg MELODIC in FSL: https://fsl.fmrib.ox.ac.uk/fsl/fslwiki/MELODIC).
What signal/noise – eg FSL’s “FIX”, trained to separate signal and noise (or use multi-echo EPI and remove ICs that not linearly dependent on TE)
For resting-state, temporal ICs are arbitrary; for subjects performing same task, can correlate the temporal ICs with predicted regressors from design matrix (to get network-level maps)
For some very stimulating tasks like movie-watching (assumed to activate most of brain), one can correlate the timeseries across subjects for “inter-subject correlation” (ISC), or even “functional normalisation” of brains

## Slide 14: ROI-based fC
Rather than using a multivariate technique across all voxels, we can calculate pairwise fC between every pair of voxels or ROIs…
Such as from a “seed” to rest of brain:

## Slide 15: ROI-based fC
Rather than using a multivariate technique across all voxels, we can calculate pairwise fC between every pair of voxels or ROIs…
Or between every pair of ROIs in an Atlas, to construct a “connectome”:

## Slide 16: ROI-based fC
Rather than using a multivariate technique across all voxels, we can calculate pairwise fC between every pair of voxels or ROIs
A common measure of fC is Pearson’s correlation coefficient (though other alternatives include partial correlation, mutual information, Granger, multi-dimensional similarity…)
However, the timeseries for any pair of voxels/ROIs can have a high correlation owing to non-interesting confounds like motion, breathing, etc…
…so we often need to “clean” the data first

## Slide 17: Motion Artefacts
CSF
TR
WM
GS
6 motions
3 spikes
Highpass
Add low (band-pass) filter (eg 0.1 Hz)?
Covary WM/CSF/Global Signal
“Scrubbing” (removing volumes with high motion), but ignores temporal autocorrelation
Rather than remove data, regress out motion parameters, including derivatives, second-order expansions (Volterra expansion), etc
Spikes = extreme values (high order expansion) – model as separate regressors

## Slide 18: Motion Artefacts
Add low-pass filter (eg 0.1Hz)?
Covary WM/CSF/Global Signal
“Scrubbing” (removing volumes with high motion), but ignores temporal autocorrelation
Rather than remove data, regress out motion parameters, including derivatives, second-order expansions (Volterra expansion), etc
Spikes = extreme values (high order expansion) – model as separate regressors
Or define spikes in wavelet domain (but what threshold?)
Patel & Bullmore (2014) Neuroimage
Signal
Noise

## Slide 19: Physiological Artefacts
High-pass filter, eg to 0.01Hz (since many biorhythms aliased to lower frequency)
If recorded physiological signals (eg cardiac, respiratory), then can adjust for (Fourier expansion of) those signals (RETROICOR)
  PhysIO toolbox https://www.tnu.ethz.ch/en/software/tapas/documentations/physio-toolbox
Or can use mean (or first few principal components) of signal in CSF/WM (though care not correlated with GM signal)
  CONN toolbox (Matlab/SPM): https://web.conn-toolbox.org/
“Global” artifacts, using “global signal regression” (eg across all ROIs)
  Pros/Cons discussed in https://doi.org/10.1016/j.neuroimage.2016.11.052

## Slide 20: Task-based fC
One way minimise confounds is to compare fC across two or more tasks/conditions. Two main approaches:
  Beta-Series Correlation/Regression (BSR): correlate Betas (trial-wise parameter estimates from single-trial model) across ROIs, and compare correlation coefficients/regression slopes across conditions
  Psycho-Physiological Interactions (PPIs): construct a model (GLM) of fMRI timeseries with regressors for 1) conditions (“psychological”), 2) timeseries from one ROI (seed) (“physiological”) and 3) the interaction between 1+2 (the key PPI term), and test significance of interaction term
See Masharipov et al 2024 for comparison: https://www.nature.com/articles/s42003-024-07088-3

## Slide 21: 1. BSR
One problem with BSR is how to estimate single-trial responses for event-related designs with short SOAs:
Bottom line: LSS better when scan noise higher than trial variability (normally the case); LSA better when trial variability higher than scan noise (see “efficiency” notebook)
http://dx.doi.org/10.1016/j.neuroimage.2015.11.009

## Slide 22
SPM{Z}
Attention
(psy)
V1
(phy)
V5
attention
no attention
V1 activity
V5 activity
time
V1 activity
Parametric, factorial design, in which one factor is psychological (eg attention)
...and other is physiological (viz. activity extracted from a brain region of interest)
2. PPIs

## Slide 23
SPM{Z}
attention
no attention
V1 activity
V5 activity
time
V1 activity
V1
(phy)
Att
(psy)
V1 x Att
(PPI)
0 0 1
2. PPIs

## Slide 24
PPI term is:
True neural interaction is:
While:
when is low-frequency (e.g, blocked)...
...not case when high-frequency (e.g., event-related)
So PPI only really suitable for slow (blocked) designs (“gPPI” option, but no true deconvolution – need forward model like in DCM...)
(Similar problem with “Beta-series regression” – where short SOAs make separation of neural activity tricky...)
2. PPI problem with brief psychological factors...

## Slide 25: Effective-connectivity: Definitions of Causality?
Direct experimental interventions (e.g, lesion, drugs)
Indirect experimental manipulations (e.g, PPI, DCM)
Network model inference (e.g, SEM, DCM)
Temporal precedence (e.g, Granger Causality, DCM)
…

## Slide 26: Effective-connectivity: Definitions of Causality?
Direct experimental interventions (e.g, lesion, drugs)
Indirect experimental manipulations (e.g, PPI, DCM)
Network model inference (e.g, SEM, DCM)
Temporal precedence (e.g, Granger Causality, DCM)
…

## Slide 27
No connection between B and C,
yet B and C correlated because of common input from A, eg:
A = V1 fMRI time-series
B = 0.5 * A + e1
C = 0.3 * A + e2
Correlations:
A B C
1
0.49 1
0.30 0.12 1
A
B
C
0.49
0.31
-0.02
2=0.5, ns.
Functional connectivity
Effective connectivity
Functional vs Effective connectivity
Partial Correlation is approximate way

## Slide 28: 3. Explicit Network Models of Causality
(Bivariate) correlations do not use an explicit network (graph) model
Can use partial correlation to adjust for all other connections within a graph (Smith et al, 2011; but often requires regularisation and can remove true connections)
Multivariate methods like Structural Equation Modelling (SEM) can test different network models, by simply comparing predicted with observed covariance matrices, but...
  has no dynamical model (stationary covariances)
  has no neural-BOLD model
  cannot test some graphs, eg loops (no temporal definition of direction)
  restricted to classical inference comparing nested models

## Slide 29: Effective-connectivity: Definitions of Causality?
Direct experimental interventions (e.g, lesion, drugs)
Indirect experimental manipulations (e.g, PPI, DCM)
Network model inference (e.g, SEM, DCM)
Temporal precedence (e.g, Granger Causality, DCM)
…

## Slide 30: 4. Temporal definition of Causality
Stationary
(correlations, SEM)
Dynamic
(Granger, DCM)
Time
(“unfolding” in time is one way to infer direction of connectivity)

## Slide 31: 4. Note on temporal causality and fMRI
Problem with time-based measures of connectivity arises with fMRI: BOLD timeseries is not direct reflection of Neural timeseries
  (e.g, peak BOLD response in motor cortex can precede that in visual cortex in a visually-cued motor task, owing to different neural-BOLD mappings)
This compromises methods like Granger Causality and Multivariate Auto-Regressive models (MAR) that operate directly on fMRI data (Friston, 2010; Smith et al, 2011)
(Note that this does not preclude these methods (eg MAR) for MEG/EEG timeseries, assuming these are more direct measures of neural activity)

## Slide 32: => Development of DCM
Dynamic: based on first-order differential equations
  - at level of neural activity, with separate haemodynamic model for fMRI
Causal: based on explicit directed graph models
Modelling: designed to test experimental manipulations
- “bilinear” approximation to interactive dynamics
4. (Estimated in a Bayesian context, allowing regularized estimation through priors, formal comparison of any number/type of models, etc...)

## Slide 33: Rough comparison of popular methods?
 | Experimental modulation | Temporal/ Dynamical | Network model | Haemodynamic Model (for fMRI)
Correlation / ICA / PCA |  |  |  | 
BSR / PPI | Y |  |  | 
Granger |  | Y |  | 
SEM |  |  | Y | 
DCM | Y | Y | Y | Y

## Slide 34: Other types of fC (not covered here)
  Multi-dimensional (pattern-based) fC (e.g., Basti et al., 2020, https://doi.org/10.1016/j.neuroimage.2020.117179)
  Dynamic fC (e.g moving windows or Hidden Markov Models, eg review: https://pmc.ncbi.nlm.nih.gov/articles/PMC3807588/)